## Slide 1: MPPT algorithm for calculating the maximum power of a photovoltaic system
Renewable Energy Smart Management

## Slide 2: Problem description
This presentation focuses on solving an optimization problem related to a parallel-series configuration of photovoltaic (PV) panels to maximize power generation. The objective is to identify the optimal voltage value that achieves maximum power output. Throughout the presentation, the techniques employed and the results obtained will be analyzed, highlighting the advantages of this solution and potential applications in the field of solar energy. The focus will be on the approach used to optimize the performance of photovoltaic systems and the potential benefits that arise from it.

## Slide 3: Problem outline
Mesure the I-V curve for each panel
Make a I-V curve for a string of panel
Make an optimization for the parallel of N strings
Plot the results starting from the single I-V curve to the optimized power result.

## Slide 4: Code structure
For the implementation of the system and optimization modules, 4 classes and a utility library were required:
PVpanel
PVstring
PVparallel
PVsimulator
PVutils

## Slide 5: PVpanel class
Starting from a set of parameters and a pair of operating conditions (G, T)
The single I-V curve of the photovoltaic panel is produced by measuring the current at the terminals as the voltage varies.
Input
Output

## Slide 6: PVstring class
The PVpanel class is utilized to construct a new class for defining a series string of photovoltaic panels. In particular, thanks to the ability to create a list of objects.
An output is generated consisting of a list of PVpanel objects and a total I-V curve of all the panels in series.
Input
Output

## Slide 7: PVparallel class
Having a class for strings available, we can connect these PV strings in parallel to increase the total power output.
In particular, a method is constructed to optimize the selection of voltage in order to maximize the power output of the system.
Input
Output

## Slide 8: PVutils class
There are problems in both the string and parallel configurations:
In the PVString class, there is a need to interpolate the total curve as it is initially composed of a series of points.
In the PVparallel class, on the other hand, it is necessary to extract data from precise reports in CSV format.
The result is the development of two methods that address these two encountered problems.
Input
Output

## Slide 9: PVsimulator class
In conclusion, a General and Modular Simulation class is created to generate a series of data on the power generated by the photovoltaic system.
In particular, the result will be plots generated by the various classes mentioned earlier and invoked during the simulation.
Input
Output

## Slide 10: Shadow zone creator - 1
To generate more realistic simulations and evaluate the increase or decrease in system performance caused by various environmental and weather conditions, a kind of mismatch generator is also used between the different panels within a string or across the entire parallel configuration, as shown in the figures.

## Slide 11: Shadow zone creator - 2
By implementing a time-varying simulation of the cloud positions that create shading on the panels, it will be possible to observe significant changes in power production compared to the previous static variations.

## Slide 12: I-V Curve for the PV
The I-V (current-voltage) curve is a graphical representation that shows the relationship between the current and voltage outputs of a solar panel or any electronic device. It provides valuable information about the panel's performance, efficiency, and power generation capabilities.
Results without Shadow - 1

## Slide 13: The Series I-V Curve
The I-V (current-voltage) curve for a series of PV (photovoltaic) panels represents the relationship between the current and voltage outputs when multiple panels are connected in a series configuration. It helps assess the combined performance and power generation of the interconnected panels.
Results without Shadow - 2

## Slide 14: The Parallel Power curve
A parallel configuration of PV (photovoltaic) panels involves connecting multiple panels side by side, with their positive terminals connected together and negative terminals connected together. This setup increases the overall current output while maintaining the same voltage level, resulting in higher power generation capacity.
Results without Shadow - 3

## Slide 15: The P-V curve for the critical points
At every hour, optimization is calculated, and therefore we can also construct the individual P-V curve for each optimization to display the chosen peak.
Results without Shadow - 4

## Slide 16
Results with Shadow on a single String - 1
String Ampere [A]
String Ampere [A]
String Ampere [A]

## Slide 17: Results with Shadow on a single String - 2
It is noticeable that, unlike case 1, the presence of a second peak of lesser magnitude indicates a difference in power generated at different voltage values, which could represent a possible maximum of optimization, albeit local.

## Slide 18
Results with Shadow on a single String - 3
The optimized voltage remains the same as in the shade-free case, as it is easily understood that in a parallel configuration, the voltage is shared among all components. Therefore, even if one of the three strings is turned off, the voltage remains unchanged. What varies, of course, is the amount of power produced during the day.

## Slide 19: Results with Shadow on a single - 1

## Slide 20: Results with Shadow on a single - 2
In this case, unlike case 1, the presence of a second peak of lesser magnitude indicates a difference in power generated at different voltage values, which could represent a possible maximum of optimization, albeit local

## Slide 21: Results with Shadow on a single - 3
It can be observed that the power chosen by the optimizer is precisely the higher one among the two peaks in the previously shown P-V plot, which displayed two maximum power points.

## Slide 22: Results with Dynamic Shadow - 1
By following the arrows, you can observe the changing conditions of the various panels in the strings.
String 1 – Panel 1 shaded
String 1 – Panel 1 shaded
String 2 – Panel 1 shaded
String 2 – Panel 1 shaded
String 3 – Panel 1 shaded
String 2 – Panel 1,2 shaded
String 3 – Panel 1,2 shaded

## Slide 23: Results with Dynamic Shadow - 2
String 1 – Panel 1 shaded
String 1 – Panel 1 shaded
String 2 – Panel 1 shaded
String 2 – Panel 1 shaded
String 3 – Panel 1 shaded
String 2 – Panel 1,2 shaded
String 3 – Panel 1,2 shaded
As it was easy to deduce from the previous graphs, multiple peaks can be observed, which are obviously due to the presence of mismatch conditions among the various panels.

## Slide 24: Results with Dynamic Shadow - 3

## Slide 25: Conclusions
In conclusion, this project has successfully addressed the optimization problem associated with a parallel-series configuration of photovoltaic (PV) panels in order to maximize power generation. By identifying the optimal voltage value that achieves maximum power output, the project has demonstrated an effective approach to optimizing the performance of photovoltaic systems.
Additionally, the project considered the impact of mismatch conditions among the panels within the parallel strings. By evaluating the system's behavior under varying mismatch conditions, valuable insights were gained into the robustness and adaptability of the proposed solution. This analysis contributes to a better understanding of real-world scenarios and the potential challenges that may arise in practical PV installations.
Overall, this project offers a comprehensive exploration of optimizing PV panel configurations and their performance under different conditions. The findings provide valuable insights for researchers, engineers, and industry professionals, fostering advancements in solar energy technologies and facilitating the widespread adoption of efficient and reliable photovoltaic systems.

## Slide 26: Bibliography